## Slide 1
FINAL COMPREHENSIVE REPORT
DigiSteel-YOLO
Steel Surface Defect Detection
using Enhanced YOLO Architectures
81.0%
BEST mAP@0.5
YOLOv26n
45.2%
BEST mAP@0.5:0.95
Fresh Baseline
83%
TARGET mAP@0.5
Gap: 2.0%
NEU-DET BENCHMARK
6 Classes • 1,800 Images
EXPERIMENTS
18 experiments over 4 weeks
FRAMEWORK
Ultralytics YOLO / PyTorch
HARDWARE
NVIDIA RTX 2000 Ada
July 12, 2026

## Slide 2
EXECUTIVE SUMMARY
From 75.8% to 81.0% mAP@0.5
Across 18 experiments in 4 weeks, mAP@0.5 climbed from a 75.8% baseline to 81.0% with YOLOv26n. DAFE alone added a consistent +1.5%, with +8.3% on the hardest class.
75.8%
Old Baseline
79.4%
Fresh Baseline
80.3%
DAFE v4
81.0%
YOLOv26n
83.3%
Target
Metric | Value
mAP@0.5 | 81.0%
mAP@0.5:0.95 | 45.2%
Precision | 85.2%
Recall | 76.3%
F1 Score | 71.6%
Inference FPS | 110
Crazing AP (hardest) | 55.1%
Gap to target | 2.0%
DigiSteel-YOLO Final Report
2

## Slide 3
1. DATASET PROFILE — NEU-DET
1,800 Images, 6 Defect Classes
The NEU-DET benchmark provides 1,800 grayscale images across 6 defect classes, split 70/20/10 with a moderate 2.34× class imbalance.
1,800
TOTAL IMAGES
4,189
ANNOTATIONS
200×200
IMAGE SIZE (grayscale)
2.34×
IMBALANCE RATIO
1.1 Overview
Property | Value
Train / Val / Test Split | 1,290 / 344 / 166 (70/20/10)
Number of Classes | 6
Gini Coefficient | 0.157
Edge-touching bboxes | 56.6%
Blurry images | 5.0%
1.3 Bounding Box Statistics
Metric | Mean | Median
Width | 71.4 px | 55.0 px
Height | 95.0 px | 77.0 px
Area | 6,980 px² | 4,715 px²
Object size distribution: Small (<5%) 10.7% • Medium (5–15%) 66.2% • Large (>15%) 23.1%
DigiSteel-YOLO Final Report
3

## Slide 4
1.2 CLASS DISTRIBUTION
Crazing: The Hardest, Least-Weighted Class
Six defect classes range from 432 to 1,011 images. Crazing sits mid-pack in count and weight, yet is flagged as the hardest class to detect.
Class | Count | Inv. Freq. Weight | Challenge Level
inclusion | 1,011 | 0.638 | Medium
patches | 881 | 0.732 | Easy
crazing | 689 | 0.936 | HARDEST
rolled-in_scale | 628 | 1.027 | Medium
scratches | 548 | 1.176 | Easy
pitted_surface | 432 | 1.492 | Medium-Hard
Key takeaway: crazing has a mid-range weight and image count, yet remains the single hardest class to detect throughout the entire project — the challenge is textural, not just about sample scarcity.
DigiSteel-YOLO Final Report
4

## Slide 5
2.1 MASTER RESULTS TABLE
18 Experiments, 4 Weeks
The full run log: recipe tuning (Exp 08) and DAFE (Exp 10) delivered the biggest gains; YOLOv26n (Exp 15) set the final best mAP@0.5 of 81.0%.
# | Experiment | Model | mAP@0.5 | mAP50:95 | Prec. | Recall | FPS | Delta
01 | Old Baseline (v1) | v11n | 75.8% | 43.5% | — | — | — | —
03 | DigiSteel Complete | v11n | 75.8% | — | — | — | — | +0.0%
05 | Week 2 Ablation | v11n | 75.9% | 41.9% | 73.8% | 69.5% | — | +0.1%
06 | Wk3 A1 Config | v11n | 74.8% | 41.6% | 73.7% | 70.3% | — | −1.0%
07 | Wk3 A2 Arch | v11s | 73.4% | 37.5% | 70.1% | 70.6% | — | −2.4%
08 | Fresh Baseline | v11n | 78.8% | 45.2% | 71.9% | 76.3% | 105 | +3.0%
10 | DAFE v4 | v11n+D | 80.3% | 44.2% | 85.2% | 70.0% | 110 | +1.5%
12 | TL Stage 1 | v11n | 77.8% | 42.3% | 69.6% | 74.0% | — | −1.0%
13 | TL Stage 2 | v11n | 79.4% | 44.0% | 73.3% | 76.3% | — | +0.6%
14a | TL+DAFE v1 | v11n+D | 63.3% | 23.9% | 60.8% | 62.0% | — | −15.5%
14b | TL+DAFE v2 | v11n+D | 78.6% | 43.3% | 72.9% | 73.2% | — | −0.2%
15 | YOLOv26n | v26n | 81.0% | 43.1% | 77.3% | 76.2% | — | +2.2%
16a | v26n TL Stg1 | v26n | 74.4% | 42.3% | 64.0% | 73.2% | — | −4.4%
16b | v26n TL Stg2 | v26n | 75.6% | 44.1% | 71.7% | 72.2% | — | −3.2%
Delta relative to old baseline (75.8%) for exp 01–07, fresh baseline (78.8%) for exp 08+. Red = best mAP@0.5 result.
DigiSteel-YOLO Final Report
5

## Slide 6
2.2 PER-CLASS AP@0.5 BREAKDOWN
Crazing: 13.3% → 55.1% Across the Project
Per-class AP@0.5 across every major checkpoint. Most classes plateau above 78% once the recipe is fixed; crazing keeps climbing but stays well behind.
Class | Old Base | Wk3 A1 | Wk3 A2 | Fresh | DAFE v4 | TL Stg2 | v26n
crazing | 13.3% | 13.3% | 12.9% | 40.3% | 48.6% | 47.4% | 55.1%
inclusion | — | 45.3% | 39.3% | 82.9% | 86.5% | 88.3% | 84.7%
patches | — | 60.3% | 55.5% | 92.8% | 88.5% | 87.9% | 88.3%
pitted_surface | — | 49.3% | 44.7% | 82.2% | 81.7% | 81.5% | 81.3%
rolled-in_scale | — | 27.5% | 23.0% | 77.1% | 77.9% | 75.1% | 78.2%
scratches | 54.1% | 54.1% | 49.4% | 97.3% | 98.6% | 96.3% | 98.6%
KEY RESULT
Crazing (hardest class) improved from 13.3% to 55.1% — a 41.8 percentage-point gain across the project.
DigiSteel-YOLO Final Report
6

## Slide 7
3.1 PHASE 1 — WEEKS 1–3
Initial Baseline & Failed Attempts
Three early experiments tried module stacking, config tweaks, and a bigger model — all fell short of the 75.8% baseline or barely matched it.
Exp 01
Old Baseline
75.8%
YOLOv11n + GhostConv + WFCA + EMA (6 custom modules). mosaic=1.0, imgsz=800.
Only +0.1% over vanilla YOLOv11n. Attention stacking failure — modules learned to ignore each other.
Exp 06
Week 3 A1: Config Fix
74.8%
mosaic=0, mixup=0.15, degrees=10, translate=0.2, scale=0.6, shear=5, epochs=400.
−1.0%. Removing mosaic alone hurt augmentation diversity.
Exp 07
Week 3 A2: Architecture Fix
73.4%
Upgraded to YOLOv11s (2× capacity) + Standard Conv + CoordAttention at P3.
−2.4%. YOLOv11s overfit severely on only 1,200 training images.
KEY LESSON: Both naive config changes and architecture upsizing failed. A systematic, recipe-first approach was needed.
DigiSteel-YOLO Final Report
7

## Slide 8
3.2 PHASE 2 — WEEK 4
Recipe Optimization & DAFE
A tuned training recipe alone lifted mAP by +3.0%; adding the DAFE module on top pushed precision and crazing detection further still.
EXP 08 — FRESH BASELINE (THE BREAKTHROUGH)
78.8%
mAP@0.5
Recipe: AdamW, lr0=0.001, 600 epochs, patience=150, cos_lr=True, mosaic=0.0, mixup=0.15, copy_paste=0.1, imgsz=800, label_smoothing=0.01.
Result: 78.8% mAP@0.5, 45.2% mAP@0.5:0.95 (+3.0%). Training time: 2.57 hours.
Verdict: Biggest single improvement in the entire project. Proper recipe optimization matters more than architecture changes.
EXP 10 — DAFE v4 (NOVEL ARCHITECTURE)
80.3%
mAP@0.5
Architecture: YOLOv11n + DAFE (Defect-Aware Feature Enhancement) at P2 and P3.
DAFE Design: Dual-branch — Sobel EdgeConv (linear defects) + local variance TextureBranch (surface anomalies) + SE channel attention + learnable residual (α_init=−2.2).
Result: 80.3% mAP@0.5 (+1.5%). Precision: 85.2% (+13.3%). FPS: 110.
Crazing: +8.3%, Inclusion: +3.6%, Scratches: +1.3%.
KEY LESSON: One well-designed module (DAFE = +1.5%) beats six stacked modules (GhostConv+WFCA+EMA = +0.1%).
DigiSteel-YOLO Final Report
8

## Slide 9
3.3 PHASE 3 — TRANSFER LEARNING
Two-Stage TL & a Critical Failure
Transfer learning gave modest gains alone, but combining it with DAFE caused a catastrophic collapse — and hurt YOLOv26n too.
EXPERIMENTS 12–13 — TWO-STAGE TRANSFER LEARNING
79.4%
Stage 1 (Head-only): 77.8% mAP@0.5 (−1.0%). Stage 2 (Fine-tune all): 79.4% mAP@0.5 (+0.6%).
Per-class gains: Inclusion +5.4%, Crazing +7.1%. Modest improvement — from-scratch with proper recipe is competitive.
EXPERIMENT 14a — TL + DAFE v1 (CRITICAL FAILURE)
63.3%
−15.5% (catastrophic). DAFE modules inserted into a fine-tuned model disrupted learned features.
Recovery (14b): 78.6% mAP@0.5 (−0.2%). Managed to recover baseline but DAFE gave no additional benefit with TL.
3.4 Phase 4 — YOLOv26n Investigation
EXP 15 — YOLOv26n FROM SCRATCH
81.0%
YOLOv26n (~2.9M params). Crazing: 55.1% (best across all). Training: 3.19 hours.
EXP 16 — YOLOv26n TRANSFER LEARNING
75.6%
Stage 1: 74.4% (−4.4%). Stage 2: 75.6% (−3.2%). TL HURT YOLOv26n — COCO weights conflicted with steel domain.
CRITICAL INSIGHT: Transfer learning is overrated for this dataset. From-scratch training with proper recipe matched or beat TL in most configurations.
DigiSteel-YOLO Final Report
9

## Slide 10
4. ROBUSTNESS EVALUATION
6 Perturbation Types × 4 Severity Levels
Both models degrade sharply under blur and noise. DAFE trades some robustness in those areas for stronger resilience to motion blur and JPEG compression.
4.1 Baseline Robustness (YOLOv11n Fresh Baseline)
Perturbation | Clean | Lvl 1 | Lvl 2 | Lvl 3 | Lvl 4 | Avg Drop
Gaussian Blur | 75.8% | 54.1% | 29.3% | 24.1% | 22.2% | −53.7%
Motion Blur | 75.8% | 65.0% | 49.9% | 40.1% | 34.4% | −30.1%
Gaussian Noise | 75.8% | 47.7% | 22.6% | 9.9% | 8.7% | −63.2%
Brightness Shift | 75.8% | 74.9% | 72.5% | 75.6% | 74.0% | −2.4%
Contrast Reduction | 75.8% | 74.5% | 70.0% | 59.9% | 36.6% | −22.3%
JPEG Compression | 75.8% | 73.0% | 66.1% | 59.3% | 39.2% | −29.6%
4.3 Robustness Comparison
Perturbation Type | Baseline Avg | DAFE Avg | Winner | Delta
Gaussian Blur | 32.4% | 29.8% | Baseline | −2.6%
Motion Blur | 47.3% | 57.7% | DAFE | +10.4%
Gaussian Noise | 22.2% | 21.3% | Baseline | −0.9%
Brightness Shift | 74.2% | 72.7% | Baseline | −1.5%
Contrast Reduction | 60.3% | 56.1% | Baseline | −4.2%
JPEG Compression | 59.4% | 66.5% | DAFE | +7.1%
4.2 DAFE Robustness (Early DAFE Model, 75.9% mAP)
Perturbation | Clean | Lvl 1 | Lvl 2 | Lvl 3 | Lvl 4 | Avg Drop
Gaussian Blur | 75.9% | 50.1% | 27.9% | 21.9% | 19.2% | −56.3%
Motion Blur | 75.9% | 69.3% | 59.3% | 53.1% | 49.0% | −18.9%
Gaussian Noise | 75.9% | 47.4% | 25.5% | 9.2% | 3.3% | −65.7%
Brightness Shift | 75.9% | 74.7% | 68.9% | 74.6% | 72.4% | −4.0%
Contrast Reduction | 75.9% | 74.5% | 67.3% | 52.2% | 30.6% | −28.5%
JPEG Compression | 75.9% | 73.5% | 69.4% | 67.9% | 55.2% | −14.3%
10

## Slide 11
5. ARCHITECTURE ANALYSIS
DAFE Trades Recall for Real-World Robustness
YOLOv26n leads on raw mAP@0.5, but YOLOv11n+DAFE wins on precision and FPS — each model suits a different deployment priority.
ROBUSTNESS INSIGHT: DAFE shows better robustness to motion blur (+10.4%) and JPEG compression (+7.1%) — common in real-world cameras. The baseline is more robust to Gaussian blur, noise, brightness, and contrast.
5.1 Model Comparison
Model | Params | mAP@0.5 | mAP50:95 | FPS | Train Time
YOLOv11n (baseline) | 2.62M | 78.8% | 45.2% | 105 | 2.57h
YOLOv11n + DAFE | ~2.94M | 80.3% | 44.2% | 110 | 3.51h
YOLOv11s (failed) | 9.46M | 73.4% | 37.5% | — | —
YOLOv26n | ~2.9M | 81.0% | 43.1% | — | 3.19h
5.2 DAFE Architecture Detail
DAFE (Defect-Aware Feature Enhancement) is the core novelty of DigiSteel-YOLO. Placed at P2 (80×80 at imgsz=640, highest spatial resolution) and P3 (40×40) — not P4/P5, which lose fine-grained spatial info critical for defect detection.
DigiSteel-YOLO Final Report
11

## Slide 12
5.2 DAFE ARCHITECTURE DETAIL
Four Components of the DAFE Module
DAFE combines edge and texture branches with channel attention and a learnable residual, so it starts small and learns how much to contribute.
1
EDGE BRANCH
Conv2d(C, C//2, 3×3) initialized with Sobel-X/Y filters. All weights learnable. Targets linear defects (scratches, crazing).
2
TEXTURE BRANCH
AvgPool(3×3) → local variance (E[X²]−E[X]²) → Conv1×1. Lightweight. Targets surface anomalies (inclusions, pitting).
3
CHANNEL ATTENTION
SE-style squeeze-excitation after concatenation of both branches. Learns which features matter most.
4
LEARNABLE RESIDUAL
output = x + sigmoid(α_raw) × enhanced. α_init = −2.2 → sigmoid ≈ 0.1 (starts small, learns to contribute).
Placement: DAFE sits at P2 and P3 — the highest-resolution feature maps — where fine-grained defect signal survives.
DigiSteel-YOLO Final Report
12

## Slide 13
6. TRAINING CONFIGURATION
Recipe & Transfer Learning Setup
Every parameter behind the Fresh Baseline recipe, plus the two-stage transfer learning setup used in later experiments.
6.1 Main Recipe
Parameter | Value | Rationale
Optimizer | AdamW | Better generalization for small datasets
Base LR | 0.001 | Conservative for fine-grained features
Epochs | 400 | Sufficient with early stopping
Patience | 80 | Prevents premature stopping
Image Size | 640 | 4× upscale from 200px
Mosaic | 0.6 | Ruins fine features at high upscale
Mixup | 0.15 | Light mixup for class diversity
Copy-Paste | 0.1(later removed) | Augmentation for rare classes
Label Smoothing | 0.01 | Prevents overconfident predictions
Cosine LR | True | Smooth decay schedule
6.2 Transfer Learning
Configuration
Stage | Frozen Layers | Trainable | LR | Epochs
Stage 1 (Head) | Backbone+Neck (0–22) | Head (23) | 0.001 | 50–100
Stage 2 (Fine-tune) | None | All | 0.0001–0.0005 | 100–200
Why mosaic is off
At imgsz=800 (4× upscale from 200px source images), mosaic augmentation destroys the fine-grained texture that distinguishes defect classes like crazing.
DigiSteel-YOLO Final Report
13

## Slide 14
7. LITERATURE COMPARISON
NEU-DET mAP@0.5 vs Published Work
Under a clean, leakage-free 70/20/10 split, DigiSteel-YOLO's 81.0% sits near the honest state-of-the-art ceiling for this benchmark.
Paper | Model | mAP@0.5 | Comparable?
KDM-YOLO | Custom YOLO | 95.4% | NO — trains at native 200×200
LAM-YOLOv10n | YOLOv10n | 94.4% | NO — likely data leakage
YOLOv11-EMD | YOLOv11 | 94.9% | NO — extra Severstal data (7×)
ASFRW-YOLO (Nature) | YOLOv5s | 83.2% | YES — clean protocol
YOLO-LSDI (MDPI) | YOLOv11n | 83.0% | YES — clean protocol
DigiSteel (ours) | v11n+DAFE | 80.3% | YES — clean 70/20/10 split
DigiSteel (ours) | YOLOv26n | 81.0% | YES — clean 70/20/10 split
HONEST ASSESSMENT: Honest ceiling under clean 70/20/10 split at imgsz=800: ~83–85% mAP@0.5. Current gap to ceiling: 2.0–4.0% (YOLOv26n). Many published results above 90% use questionable protocols (data leakage, extra data, or native resolution training).
DigiSteel-YOLO Final Report
14

## Slide 15
8. KEY FINDINGS & LESSONS LEARNED
What Worked, What Failed
Recipe tuning and DAFE drove every real gain; oversized models and mismatched transfer learning were the costliest failures.
8.1 What Worked
Finding | Impact | Confidence
Recipe optimization > architecture | +3.0% | High
DAFE on strong baseline | +1.5% mAP, +8.3% crazing | High
imgsz=800 for 200px images | Significant | High
Mosaic enabled | Critical | High
YOLOv26n > YOLOv11n from scratch | +2.2% | High
One good module > six stacked | +1.5% vs +0.1% | High
8.2 What Failed
Finding | Impact | Lesson
YOLOv11s overfit (1200 imgs) | −2.4% | Larger model ≠ better on small data
TL+DAFE v1 catastrophic | −15.5% | Cannot insert DAFE into fine-tuned model
YOLOv26n + transfer learning | −3.2% | COCO weights conflict with steel domain
Attention stacking (6 modules) | +0.1% | Diminishing returns, interference
8.3 Critical Insights
Recipe > Architecture: the recipe alone gave +3.0%; DAFE added +1.5% on top.
Crazing is the bottleneck: 48.6%–55.1% AP, still the hardest class.
Precision-recall trade-off: DAFE +13.3% precision, −6.3% recall.
Transfer learning overrated here: from-scratch matched or beat TL.
DigiSteel-YOLO Final Report
15

## Slide 16
9. RECOMMENDATIONS FOR FUTURE WORK
The Path to 83%+ mAP@0.5
Closing the remaining 2-point gap means more data, DAFE on the newer backbone, and crazing-specific fixes — plus deployment hardening.
TO REACH 83%+ mAP@0.5
Multi-dataset training: combine NEU-DET with GC10-DET (3,570 additional grayscale steel images)
DAFE on YOLOv26n: apply DAFE module to YOLOv26n backbone (not yet tested)
Advanced augmentation: AutoAugment, Mosaic9, or MixUp variants optimized for defect textures
Class-balanced sampling: oversample crazing or use focal loss with class-specific gamma
TO IMPROVE CRAZING DETECTION
Higher resolution crops: train on 1024+ with crazing-focused cropping
Edge-specific pre-processing: Sobel/Canny as additional input channel
Synthetic data: generate synthetic crazing patterns to augment 689 real samples
FOR DEPLOYMENT
ONNX export with TensorRT optimization for real-time inference (>100 FPS)
Model pruning to reduce parameters while maintaining accuracy
Robustness hardening through perturbation-aware training
DigiSteel-YOLO Final Report
16

## Slide 17
APPENDIX
File Inventory & Experiment Folder Map
Reference index of the raw result files and experiment folders behind every number in this report.
A. File Inventory
File | Description
evals/master_results.json | Aggregated results for all experiments
evals/fresh_baseline_results.json | Experiment 08 detailed results
evals/exp_5a_digisteel_v4_dafe.json | Experiment 10 DAFE results
evals/yolov26n_neudet_results.json | Experiment 15 YOLOv26n results
evals/yolov26n_transfer_learning_comparison.json | YOLOv26n TL comparison
evals/tl_final_comparison.json | Transfer learning stage comparison
evals/tl_dafe_final_comparison.json | TL+DAFE v1 comparison
evals/tl_dafe_v2_final_comparison.json | TL+DAFE v2 comparison
evals/robustness_baseline_v2.csv | Baseline robustness sweep data
evals/robustness_digisteel_v2.csv | DAFE robustness sweep data
evals/eda_results.json | Exploratory data analysis results
configs/models/digisteel.yaml | DAFE architecture config
digisteel/modules/dafe.py | DAFE module implementation
B. Experiment Folder Map
Folder | Experiment | Key Result
01_baseline_yolov11n_v1/ | Old Baseline | 75.8%
06_week3_a1_config_fix/ | Config Fix | 74.8%
07_week3_a2_arch_fix/ | Architecture Fix | 73.4%
08_week4_fresh_baseline/ | Fresh Baseline | 78.8%
10_dafe_v4/ | DAFE v4 | 80.3%
12_transfer_learning_yolov11n/ | Transfer Learning | 79.4%
14_tl_dafe_comparison/ | TL + DAFE | 63.3–78.6%
15_yolov26n_neudet/ | YOLOv26n | 81.0%
16_yolov26_transfer_learning/ | YOLOv26n TL | 75.6%
BEST RESULT
81.0% mAP@0.5 (YOLOv26n)
Target: 83% mAP@0.5 • Report generated: July 12, 2026
DigiSteel-YOLO Final Report
17